Chair of Computing in Civil Engineering
Katrin Jahr	Robert Schlich
Decentralized autonomous sensor fault detection using neural networks
“Anleitung zu wissenschaftlichem Arbeiten”
[Speaker Notes: We will present a wireless structural health monitoring system, which is capable of autonomous sensor fault detection]

---
Structural health monitoring
Structural health monitoring (SHM):
“structural evaluation method
that uses any of several sensors
which are attached to [...] a structure”
Luke A. Bisby. An introduction to structural health monitoring.
Canada, 2014
[Speaker Notes: To prevent structural failure, faults and deforminities have to be detected and repaired From the outside, cracks and fractures are hard to distinguish Structural Health Monitoring is used Sensors collect data like acceleration, temperature and strains Observation over time, Determining changes in material and geometric behavior]

---
Structural health monitoring
SHM Tasks
Fault
detection
Data
acquisition
Data
processing
Data
transmission
Data
storage
Data
analysis
[Speaker Notes: Data acquisition Data processing Data transportation Data storage Data analysis]

---
Structural health monitoring
Dataflow
Sensor nodes
Neural
network
Fault
detection
Sensor
values
Data
acquisition
Natural
frequency
Data
processing
Natural
frequency
Data
transmission
Sensor nodes
Sensor nodes
Basestation
MySQL
Database
Data
storage
User
application
Data
analysis
Host computer
Host computer

---
Structural health monitoring
Data processing – frequency spectrum
[Speaker Notes: lot of data is collected Has to be processed, transmitted, stored, and analyzed Data reduction strategy: Changes in the natural frequency indicate structural changes Natural frequency is calculated, using a fast fourier transform Returns a frequency spectrum, which shows the frequencies of a vibration and their magnitudes Highest magnitude = natural frequency Data is reduced to only 2 values for every measurement Changes in highest magnitude are used for sensor fault detection]

---
Structural health monitoring
Laboratory setup
Laboratory setup	Simulated sensor fault
[Speaker Notes: Installed shm system on a test structure 4 story shear frame structure One sensor node per story Excitation by a deflection of the top of the structure]

---
Sensor fault detection
Sensor fault detection
Analytical redundancy is realized
through training neural Networks
to predict sensor measurements
[Speaker Notes: Over their lifetime, the wireless sensor nodes can become inaccurate, faulty, or may even break Analytical redundancy uses mathematical functions to compute virtual sensor measurements Virtual sensor measurements are compared to actual measurements – a deviation indicates a sensor fault Measurements = magnitudes from the FFT In this study neural networks are used to implement analytical redundancy]

---
Sensor fault detection
Neural network
[Speaker Notes: Neural networks are able to learn, to map mathematical functions Interconnected neurons communicate through weighted connections Learning is realized by adjusting weigths until the desired output is reached A neural network, is implemented into each sensor node trained to predict the magnitude of the embedding sensor node, based on the magnitudes of the other sensornodes]

---
Sensor fault detection
Mean error after training phase
[Speaker Notes: Prior to actual fault detection, training samples for the neural network must be gathered Test runs with different numbers of training samples After training 10 measurements are conducted Correlation between increasing numbers of training samples and decreasing mean error of the prediction]

---
Sensor fault detection
Sensor fault simulation
Laboratory setup	Simulated sensor fault
[Speaker Notes: A sensor fault is simulated One sensor node is: Rotated Shifted in position Mounted more loosely (red circle) Deviation of prediction and measurement is observed]

---
Sensor fault detection
Deviation after fault detection
[Speaker Notes: The Deviation increases by more than 10% in various tests The faulty sensor node is clearly distinguishable In conclusion: A neural network can be trained to predict measurements of sensor nodes with great accuracy The accuracy is sufficient to recognize sensor faults]