Chair of Computing in Civil Engineering
Katrin Jahr	Robert Schlich
Decentralized autonomous sensor fault detection using neural networks
“Anleitung zu wissenschaftlichem Arbeiten”
[Speaker Notes: We will present a wireless structural health monitoring system, which is capable of autonomous sensor fault detection]

---
Structural health monitoring
Structural health monitoring (SHM):
“structural evaluation method
that uses any of several sensors
which are attached to [...] a structure”
Luke A. Bisby. An introduction to structural health monitoring.
Canada, 2014
[Speaker Notes: To prevent structural failure, faults and deforminities have to be detected and repaired From the outside, cracks and fractures are hard to distinguish Structural Health Monitoring is used Sensors collect data like acceleration, temperature and strains Observation over time, Detemining changes in material and geometric behaviour]

---
Structural health monitoring
SHM Tasks
Fault
detection
Data
acquisition
Data
processing
Data
transmission
Data
storage
Data
analysis
[Speaker Notes: Data acquisition Data processing Data transportation Data storage Data analysis]

---
Structural health monitoring
Dataflow
Sensor nodes
Neural
network
Fault
detection
Sensor
values
Data
acquisition
Natural
frequency
Data
processing
Natural
frequency
Data
transmission
Sensor nodes
Sensor nodes
Basestation
MySQL
Database
Data
storage
User
application
Data
analysis
Host computer
Host computer

---
Structural health monitoring
Data processing – frequency spectrum
[Speaker Notes: lot of data is collected Has to be processed, transmitted, stored, and analyzed Data reduction strategy: Changes in the natural frequency indicate structural changes Natural frequency is calculated, using a fast fourier transform Returns a frequency spectrum, which shows the frequencies of a vibration and their magnitudes Highest magnitude = natural frequency Data is reduced to only 2 values for every measurement Changes in highest magnitude are used for sensor fault detection]

---
Structural health monitoring
Laboratory setup
Laboratory setup	Simulated sensor fault
[Speaker Notes: Installed shm system on a test structure 4 story shear frame structure One sensor node per story Excitation by a deflection of the top of the structure]

---
Sensor fault detection
Sensor fault detection
Analytical redundancy is realized
through training neural Networks
to predict sensor measurements

---
Sensor fault detection
Neural network

---
Sensor fault detection
Mean error after training phase

---
Sensor fault detection
Sensor fault simulation
Laboratory setup	Simulated sensor fault

---
Sensor fault detection
Deviation after fault detection